## Slide 1: 傳統車本觸動號誌設計不符合時代潮流

## Slide 2: 新式觸動號誌機制追求更公平的時制時相分配
Signal timing manual, 2nd Edition 2015
Traditional optimization tools generally focus only on simple vehicle-oriented performance measures because they are easy to quantify and, therefore, easy to “optimize.” However, vehicle stops and delay may be less important than transit and pedestrians in a CBD, as well as other existing or developing areas with significant pedestrian, bicycle, and transit activity. The practitioner needs to make appropriate adjustments to the traffic signal timing process to account for the operating environment and user priorities.
City of Redmond, WA
• Provide more equitable assignment of green time to all road users;
• Improve corridor progression;
• Improve travel time reliability;
• Improve corridor safety
Bid Postings • Adaptive Signals (Downtown Vicinity) (redmond.gov)

## Slide 3: 機會
台灣
  市場上沒有穩定可行的方案：計畫期滿即結束，延續性不足因效益不明確 (連益工程訪談)
  市場主要Player還是針對車輛進行演算法設計
    資拓於桃園設計的AI號誌未納入行人偵測 (2024智慧城市展詢問回覆)
美國

## Slide 4: Total solution package
車輛偵測
delay, 通過量
行人偵測
delay, 通過量
自行車偵測
delay, 通過量
偵測設備
Pretimed號誌時制計畫
依據初始交通調查數據設計
觸動號誌時制設計
依據偵測數據即時調變
演算法
HW+VA
績效追蹤
GVP數據追蹤路段旅行時間及路口延滯
取代VD或eTag
擴充功能：
優先通行：透過RSU+攝影機偵測優先通行車輛，即時開綠燈給予通行；納入補償機制 (訪談亞勳時探聽到台灣 (成大)現階段尚無納入)
路口資訊播送增加安全：透過RSU播送感測器蒐集資料 (sensor data sharing)、SPaT訊息 (從交控器)  V2X & AV 應用
顧問、學界

## Slide 5: 觸動號誌演算法設計公司
Q-Free MAXTIME Suite | Sophisticated traffic signal control software
Overview of SCATS Products (nsw.gov.au)
SCOOT® - TRL Software
Types of ASCT
Implementing ASCT will maximize the capacity of existing systems, ultimately reducing costs for both system users and operating agencies.
Many choices are available from many vendors, with more in development. Available adaptive signal control technologies include the Split Cycle Offset Optimization Technique (SCOOT), Sydney Coordinated Adaptive Traffic System (SCATS), Real Time Hierarchical Optimized Distributed Effective System (RHODES), and Optimized Policies for Adaptive Control (OPAC) "Virtual Fixed Cycle" and ACS Lite.
InSync developed by Rhythm Engineering (Lenexa, Kansas) combines a strategy of global and local intersection optimization methodology to improve arterial progression while reducing side street and left turn delay. There are many others in existence and in development.